## Slide 1: Train Your Batting
Divyansh Sharma
20XX

## Slide 2: How to face fast bowling?
Problem Identified
20XX
Reaction time of 200ms
Select correct shot
Select fast enough
Improve reaction time of batters
Remote practice option
Prevent fatal injuries.

## Slide 3: Data Collection
Shot | Time Taken
Cover Drive | 10 mins
Pull Shot | 10 mins
On Drive | 10 mins
Square Cut | 10 mins.
Idle | 10 mins
10mins per each shot

## Slide 8: Shot Classification Model
Feed Forward
Neural Network
IMU
Ax, Ay, Az, Gx, Gy, Gz
Cover Drive
1
On Drive
2
Cover Drive
3
On Drive
4

## Slide 9: RNN, LSTMS First Attempt
Maximum Accuracy of 74%
Time Series Data

## Slide 10: Feature Engineering and Feed Forward Neural Network
Popular method in literature for accurate results.
Features | Information
Mean | -
Standard Deviation | -
Root Mean Square | Quantifying the energy of the signal
Skewness | Assymetry of the signal. Indicative of specific type of motions
Spectral Skewness | Identifying frequency related patterns in the movement
Spectral Power in Frequency Bands | How energy is distributed among frequencies

## Slide 11: Feature Generation
1800 features
Syntiant IMU
Memory Size: 200Kb.

## Slide 12: Play Stick Cricket
Popular Cricket Game challenging the ‘reflex’ of batsman.
Aim is to replace the keyboard press with Arduino
Another objective
Marker Display
Latest Time to play
shot
0
2.8s

## Slide 13: Improvements
Select Important Features
Features that did not show any correlation with the labels are removed.
This reduces the computation and memory required by the model
Reduced from 1800 to 78 features
Full Integer Quantization
20XX
Conversion from 32bit integer to 8bit integer
Considerably reduced model size.